## Slide 1
Molten Salt Reactors and Thorium Utilisation
Prototype Fast Breeder Reactor
Monazite sand in Kerala beach
Srikumar Banerjee
Homi Bhabha National Institute
Bhabha Atomic Research Centre
Nuclear Energy Conclave, India Energy Forum
18 October, 2019

## Slide 2
Uranium +Thorium Deposit: 3,00,000 + 8,00,000 = 11,00,000 Tonnes (Metal)
Electrical Energy produced in one cycle 11,00,000 T x 60,000 MWtd/T
(With 40 % thermodynamic efficiency) 6.4 x 1014 kWh per cycle
In 10 Recycles (possible in Breeder Reactors
with Breeding Ratio~ 1.03 & 3% Loss) 6.2 x 1015 kWh
India ‘s stabilised population 1.7 x 109
Annual consumption(Today’s world average) 3000 kWh per capita
Sufficient for 1200 years, if all energy comes from nuclear
Sufficient for 6000 years, If 20 % comes from nuclear
Energy Potential of Indigenous Fissile and Fertile Materials

## Slide 3
Fuel cycle options
Closed Fuel Cycle
Fuel
Fissile+Fertile
Fissile partly spent
Fertile partly converted
Reprocessing
Nuclear Reactor
Fertile + Fissile
Long lived waste Repository
Fuel Manufacturing
Fuel
Fissile+Fertile
Fissile partly spent
Fertile partly converted
Spent Fuel Repository
Once Through Fuel Cycle
Nuclear Reactor
Huge energy potential !!

## Slide 4
232Th
233Th
233Pa
233U



Fertile
Fissile
238U
239U
239Np
239Pu



Fertile
Fissile
n
n
Conversion from Fertile to Fissile Materials

## Slide 5
Variation of η with neutron energy
Thermal neutrons absorbed in fuel
 =
Total neutrons produced in fuel due to fission

## Slide 6: Development of Molten Salt Breeder Reactors
The fuel is in the molten salt form
(Li7F, BeF2, ThF4, UF4) circulated
through the heat exchangers and
reprocessed online
Air craft Reactor Experiment
(ARE) 1954, 2 MWt
Molten Salt Reactor Experiment (MSRE)
(ORNL, 1965-1969); 8 MWt
all three fissile nuclides tested
Single Fluid MSBR (Breeding ratio 1.04) and Two fluid MSBR 1000 MWe designed (Breeding ratio 1.07) using thorium fuel
Alvin Weinberg (1915- 2006)

## Slide 7
Molten Salt Reactors (MSR)
Molten salt(Li7F, BeF2, ThF4, UF4) fuel circulated through heat exchangers and reprocessed online
Enhanced safety due to large difference between melting point and boiling point (500o C and 1400o C) near ambient operating pressure
High thermal efficiency due to high operating temperatures
On line removal of poisons and fissile addition result in gain in reactivity and neutrons- minimum excess reactivity in the reactor
As fuel is in the molten state, melt down accident is of no concern
Passive dumping of fuel by melting of freeze plug

## Slide 8
If only gaseous fission products are removed high conversion ratio of the order of 0.94 can be obtained
If all the fission products are removed and protactinium is also separated and stored separately, molten salt breeder are possible
ORNL single fluid design has B.R. ~ 1.04
ORNL two fluid design has B.R. ~ 1.07
Molten salt fast reactor design studies are also in progress as η is higher
Use of chloride may keep the spectrum harder than fluoride
Reactor Doubling Time can be of similar order in thermal breeder reactor compared to fast reactor even with smaller breeding gain due to smaller specific fissile inventory in thermal reactors
Molten Salt thermal breeder reactors will have very good fuel utilisation
Summary of Molten Salt Reactors

## Slide 9
half life of Pa233 is 27 days
Protactinium Pa233 if remains in high flux region in reactor will absorb a neutron, Pa234 will be formed which by beta decay converts to U234. So a neutron is lost and U233 is also not produced. Thus there is a double loss
U233 produced is free of U232
Advantage of protactinium removal

## Slide 10
Online removal of poisons, and protactinium enhances the conversion ratio
Single Fluid MSBR (Breeding ratio 1.04) and Two fluid MSBR 1000 MWe designed (Breeding ratio 1.07) using thorium fuel. Recent report claims, BR nearly 1.1
Breeding in Molten Salt Thermal Reactors with Thorium
No external fissile feed needed in equilibrium
Self sustaining thorium cycle
Molten Salt Reactor
Reprocessing
Fission products
Protactinium
U233
Thorium

## Slide 11
Molten Salt breeder reactor
1 ton fissile
Why Thermal Breeder is attractive?
PHWR /
AHWR
1 GWe
120 T
N. U./year
F.P
200 kg U233
+Th / year
20 T/ year Spent fuel
1 GWe
MSBR
B.R.=1.05
Reprocessing
plant
6 Ton
En. U
14 Ton Thorium
Reprocessing plant
Enrichment
plant
22 years
DoublingTime
22 years
Fast breeder reactor
4 Ton fissile
Reprocessing
PHWR
1 GWe
170 T
N. U./year
F.P
600 kg Pu
+D.U./year
170 T/year
Spent fuel
1 GWe
FBR
B.R.=1.2
Fabrication
plant
Reprocessing
plant

## Slide 12
101
102
103
104
105
106
107
108
109
101
102
103
104
105
106
107
Radiotoxicity of Spent Fuel
Decay Time (Years)
-
U235 - Pu Fuel Cycle
After Separation of TRU
U233 - Th Fuel Cycle
Natural U Ore
By virtue of being
lower in the periodic
table than uranium,
the long-lived minor
actinides in spent
fuel are in much lower
quantity with the
thorium cycle.
Thorium Fuel Cycle Reduces Nuclear Waste Burden
Radio-toxicity of spent fuel against time for U235 - Pu, U235-Pu (minor actinides removed) and Th-U233 fuel cycles
Minor actinide (g/T) | U235 + U238 | U233 +Th232
Np | 900 | 3
Am | 470 | 0.0018
Cm | 220 | 0.00064
Production of minor actinides in U and Th fuel cycle in g/t of heavy metals at 60 GWD/t
Amit Rajora, etal.,ThEC-2015, , Mumbai, India, October 12-15, 2015

## Slide 13: Some Drawbacks of MSBRs
Dimensional changes in graphite hence frequent replacement; Zirconium hydride is considered as moderator in recent designs in place of graphite
Safety parameter βeff low due to fuel circulation
Better structural materials to hold molten fluorides to prevent radioactivity leaks, Hestalloy-N was developed
Radioactivity in primary circuit, needs retention, cooling under all situations

## Slide 14
Molten Salt Reactor
Reprocessing
plant
Fission products
Protactinium decay tank
U233
Fuel salt (Th-U)
Purified
salt
Breeding in Molten Salt Thermal Reactors with Thorium
Online removal of poisons,
and protactinium enhances
the conversion ratio
Two fluid MSBR 1000 MWe
Single Fluid MSBR (Breeding ratio 1.04) and Two fluid MSBR 1000 MWe designed
(Breeding ratio 1.07) using thorium fuel. Recent report claims, B.R. nearly 1.1
Graphite

## Slide 15
Concluding Remarks
Revival of interest in Molten Salt Reactors in Several Countries
India’s special interest due to the possibility of early introduction of Thorium
Breeding possible in thermal spectrum, with doubling time comparable with fast reactors
Feasibility of Construction of a wide range of sizes
Inherently safe design
Thank You for your Attention