## Slide 1
© 2017 All rights reserved. Property of the University of Wyoming
Understanding & Extracting
the Latent Value in Coal
Beyond Non-coking coal to Coking Coal
Richard A. Horner
Director Special Projects and Emerging Technology
School of Energy Resources
University of Wyoming
Notes: Thank introduction
Thank PCC for opportunity to speak
My name is
Title

## Slide 2: Outline
Outlook for Coal in Inda
New markets
  Coking Coal
  Non energy and Fuel Products
Existing Technology Approaches
  FMC Coking
  Hyper-coal
  HHS technology
  Thermo-chemical processing
The Coal Refinery
  Thermo-chemical coal processing
Concluding Remarks

## Slide 3: Outlook for Coal in India
Coal will grow as a most important natural resource on which its economy will prosper.
Forecasts indicate that India will become the Largest Importer of Coking Coal by 2015
  Annual growth rate of 5.4% between 2019 and 2028.
[Reference: IEA Coal 2018; Analysis andFforecasts to 2023]

## Slide 4: Petrochemicals are a Growth Opportunity
[Reference Asia Petrochemical Industry Conference: India Report 2018]

## Slide 5: Coal to Non Energy & BTU Products The possibilities are vast!
Reference: US Geological Survey
© 2017 All rights reserved. Property of the University of Wyoming
Some of these chemicals and materials can only economically come from coal!
Notes: Each leaf represents a product
  Were looking at products that aren’t energy
  Some leaves can be made from coal but aren’t due to economics or environmental constraints
    Other industries like oil can make cheaper
  HOWEVER, Some of the leaves are only made from coal like cokes and creosotes
  Market and technology has made some of these products possible now, economically

## Slide 6: Summary of Coal Conversion…TODAY
© 2017 All rights reserved. Property of the University of Wyoming
Some specialty chemical products
today can only be derived from coal
Unlike crude oil, coal is not readily fractionable.
Coal constituent polycyclic hydrocarbons which readily react and polymerize.
We know how to destruct coal and how to break it down into smallest molecules to build it up again (gasification and XtoL)
  Hugely energy intensive
  No good for extraction of hiddeent value in coal
Understanding conversion behavior – thermal impacts on molecular chemistry is crucial to exploit coal’s ‘hidden’ value
Notes: Coal is readily convertible but not fractionatable
  We need to transform the coal before we can get valuable intermediates
Our coal is very reactive
There is a desire to understand conversion behavior
  Thermodynamics
  Molecular chemistry
  Find hidden value of coal

## Slide 7: Evaluating Coal Conversion Approaches
© 2017 All rights reserved. Property of the University of Wyoming
Two ways to convert coal to extract ‘hidden’ value
  Thermally
  Pyrolysis, gasification and liquefaction
  Chemically
  Solvent extraction (Single phase, Low temperature)
Factors determining coal conversion approaches to pursue
  Considerations
  oxygen in liquids/solids
    Somewhat unique to PRB Coal
  Using complementary feedstocks with coal (e.g. natural gas), to diversify the portfolio of products that can be manufactured
    Wyoming natural resource strength
  managing CO2
    Challenge for coal generally
Notes: There are two overarching ways to convert coal
  Thermally
    These methods are pyrolysis, gasification and liquefaction
      They are also chemically converting coal as well, they just are at high temperature
  Chemically
    Solvent extraction
      This is attractive because it is single phase and run at low temperatures
After considering our goals and constraints
  Allows us to reject gasification and liquefaction
  Instead, research solvent extraction and pyrolysis in NEW ways
    Get new technology and processes that haven’t been done before

## Slide 8: Kobe Steel – Upgraded Brown Coal (UBC) Process
Briquets are high calorific value, low ash coal content
Claimed to be compatible with coal fired power plants configured to run on bitumous coal

## Slide 9: De-ashing Low Rank Coal - Hyper-Coal ™
Developed between 2001-2007
Turns low-grade thermal coal into coking coal (low ash)
Solvent extracts ash and insoluble at 380 deg C.
Ash and coal fines settle out during flotation
Proven to emulate coking coal in practice
Treatment cost is $100/mt !
Very coal quality dependent

## Slide 10: Transforming Wyoming Kemmerer Sub-bitumous coal into coke for steel making
The FMC Coke Process
Kemmerer Plant showing Calciner & Cooler
[Journal of Metals, May 1966]
Upgraded sub-bitumous coal into coke
Operated 1980’s to 2002
Product shipped to USA steel industry
Plant shut down in 2002 due to tightening environmental requirements
  land contamination – phenols.

## Slide 11: Evaluating Coal Conversion Approaches
© 2017 All rights reserved. Property of the University of Wyoming
  Considerations
  Even the inorganic mineral matter has value
    Coal homogeneity is crucial as it dictates processing methodology
      Construction Materials
      Source of very valuable rare earth elements
  Delibertate decomposition of coal including use of low temperature processes is key to extraction of value
  What if we combine solvent and thermal processing?
Notes: There are two overarching ways to convert coal
  Thermally
    These methods are pyrolysis, gasification and liquefaction
      They are also chemically converting coal as well, they just are at high temperature
  Chemically
    Solvent extraction
      This is attractive because it is single phase and run at low temperatures
After considering our goals and constraints
  Allows us to reject gasification and liquefaction
  Instead, research solvent extraction and pyrolysis in NEW ways
    Get new technology and processes that haven’t been done before

## Slide 12: Thinking Synergistically Extract & Recover Value from the Mineral Matter
Solvent selection is critical and depends on coal minerology
Exploits hydrophilic and hydrophobic behavior of coal surfaces to dewater and recover moneral matter at low temeperatre

## Slide 13: Coal Refinery - Platform Level Application
Systems and Methods for Refining Coal into High Value Products
  International App. No. PCT/US18/50690
  Filed September 12, 2018
  Published WO 2019/055529
  Foundational level patent application
    Combination of Solvent Extraction and Pyrolysis
    Highly-branched, purified product distribution
  Coordinated set of extension applications
Thermo-Chemical Coal Processing

## Slide 14: Solvent Extraction Integrated Example 2 stage extraction, dry methane reforming, phenol recovery, calcining, Carbidization
Hydrocarbon Solvent Extraction
Gas Clean-Up
Coal
Gas
Phenol
Benzene. Toluene,
xylene
This is an example of how multiple technologies can be integrated into a multi-high volume product, low energy consumption & CO2 emissions complex
Flash Pyrolysis and fractionation
Light Density
Liquids
Phenol Extraction
NH3, S
CO2
Dry Methane
Reforming
NatGas
Syngas
Hi-Ash Char
Low Ash Coke
Soil Amendments
Construction Materials
© 2017 All rights reserved. Property of the University of Wyoming
Resins (Pitch, tars), fibers and surfactants
Asphaltenes (asphalts, fibers, cokes)
Medium Density
Liquids
Heavy Density
Liquids
Metallurgical materials
Electrode materials
Notes: Integrate technology to develop an early idea of a coal refinery
  Talk through the flowsheet
  Dry Methane Reforming is a way were handling the CO2 constraint.
  We use systems engineering on each box individually as well as the overall process

## Slide 15: Coal Refinery - IP Extensions
  Platform Level
  Application
  Publication WO 2019/055529
  PCT/US18/50690
  Systems and Methods for Refining Coal into High Value Products
  Filed September 12, 2018
  Extension
  App. No. 2
  GRAPHENE OXIDE USING MODIFIED HUMMER’S METHOD
  Extension
  App. No. 4
  COAL(TAR) LIQUEFACTION BY ESTERIFICATION
  Extension
  App. No. 3
  THERMO-CHEMICAL PROCESSING OF COAL WITH 1-METHYLNAPHTHALENE
  Extension
  App. No. 1
  MODIFIERS FOR ASPHALT PETROLEUM PRODUCTS FROM COAL DERIVED LIQUIDS
  Separate
  App.
  Dry methane Reforming Catalysts
  Separate
  App.
  Green Building Materials
  Separate
  App.
  Carbon Fiber
  Separate
  App.
  Silicon Carbide

## Slide 16
[ Ref: Bell Research Group, Department of Chemical Engineering, University of Wyoming]
Thermo-chemical Processing to Deliberately Decompose Coal
Objectives
Develop a thermochemical pathway to deliberately decompose coal so that the liquid yield is maximized
Validate the performance on Wyoming coal
Identify the most attractive product types and pathways to pursue
Commercialize the thermo-chemical process as the backbone of a coal refinery
Next Milestones: By end 2019,
Commission continuous flow reactor and determine coal decomposition relationship with products and properties with a mass balance. Design and construct process pilot plant based upon these findings.
Coal residue liquid extraction
Pyrolysis
drop tube experiment
Continuous flow pyrolysis reactor
asphalt products projects

## Slide 17
[ Ref: Stahl Research Group, Department of Ecosystem Science and Management, University of Wyoming]
Improve Soil Fertility in Wyoming
Objectives
Confirm that coal derived organic-chars can improve soil condition for growing crops
Understand crop growth relationship between (short term) nutrient additives & (long term) soil structure change
Synthesize coal based coal derived soil fertility improvement products using pyrolysis approaches
Validate performance of soil fertility product formulas in the field (on wheat and corn).
Coal -Pyrolysis
Soil Fertility Demonstration: May 2018
Coal derived organic char mixing with nutrient
Wyoming
PRB Coal
Greenhouse Studies

## Slide 19
High Performance
Supercapacitor
[ Ref: Li Research Group, Department of Chemical Engineering, University of Wyoming]
Manufacture of Carbon Fiber Mats
from coal derived precursors for electrical and thermal applications
Objectives
Derive & characterize coal tar and solid coal extracts to make fiber mats for electrical duties
Understand the relationship between chemistry and product performance
Make fiber mats with superior electrical performance
Validate application of products in energy storage applications
Wyoming
PRB Coal
Coal (solvent extracted)
liquid Extract
Elastic coal-based
carbon fiber mat
Capacitance Characterization
Electro-spinning
Heat-treatment
Solvent Recovery

## Slide 20
[ Ref: Tan Research Group, Department of Civil & Architectural Engineering, University of Wyoming]
Green Building Materials from Wyoming Coal
Objectives
Develop green building material formulations for coal derived intermediate products
Evaluate performance of coal based materials against building product specifications
Identify performance improvement additives and chemistry changes
Perform field trials
Heat-treatment (~500 deg. C)
Calcination
Wyoming
PRB Coal
Coal extracts (solvent)
Coal derived ‘Green’ Building
Products
carbon fiber reinforced geopolymer,
geopolymer bricks,
coal ash foam glass,
(d) coal ash silica aerogel
wall plaster
CER-500
CER-600
CER-700
CER-800
CER-900
CER-500
CER-600
CER-700
CER-800
CER-900

## Slide 21
Diamond films
produced directly from coal
[ Ref: Johnson Research Group, Department of Chemical engineering, University of Wyoming]
Manufacture of High-performance composite-resin systems and coatings from coal
Objectives
Derive high temperature resin systems from coal extracts
Extract and transform coal solid-derivatives into performance enhancing additives
Design and validate coal derived composite material solutions
Validate application of products in extended performance product duties
Wyoming
PRB Coal
Polyurethane resin systems
Graphitic Products

## Slide 22: Concluding Remarks
© 2017 All rights reserved. Property of the University of Wyoming
  Indian coal has unique properties which need to be fully understood if the hiden value is to be realized.
  Significant growth opportunities exist to use cioal as a feestock to make engineered products
    Even the recovered mineral matter has value
  Deliberate decomposition coal rather than destruction using high temperature has proven to be a viable solution to transform coal into value added products
    Application of thermo-chemical processing still to be proven on coals other than Wyoming Powder river basin (PRB) coal
Notes: There are two overarching ways to convert coal
  Thermally
    These methods are pyrolysis, gasification and liquefaction
      They are also chemically converting coal as well, they just are at high temperature
  Chemically
    Solvent extraction
      This is attractive because it is single phase and run at low temperatures
After considering our goals and constraints
  Allows us to reject gasification and liquefaction
  Instead, research solvent extraction and pyrolysis in NEW ways
    Get new technology and processes that haven’t been done before

## Slide 23: Thank You
© 2017 All rights reserved. Property of the University of Wyoming